## Slide 1: Safety Training
For SUNY Oswego Summer Staff

## Slide 2: Agenda
Hazard Communication
(Material) Safety Data Sheets
Asbestos
Personal Protective Equipment
Fire Safety
Heat Stress
Confined Space
Lockout/ Tag Out
Fall Protection/Ladders/Scaffolds
Slips, Trips, Falls
Bloodbourne Pathogens
General & Questions
https://www.osha.gov/dep/fatcat/fy15_federal-state_summaries.pdf

## Slide 3: Facility Services Org Chart
AVP
EHS
MP
M&O

## Slide 4: Facility Services Safety

## Slide 5: FS Reporting Safety Concerns
AVP
EHS
MP
M&O
Notes: Chain of Command
Check with Supervisor
Check with Their Supervisor
Director – Mary then me, then Mitch,
Then OSHA (PESH)

## Slide 6: Format for Safety Topics
Regulatory Overview
What you need to know

## Slide 7: Hazard Communication Regulations
“Employees have both a need and a right to know the hazards they are exposed to when working”
Components of HAZCOM – OSHA 29CFR 1910.1200
  Written program - https://www.oswego.edu/facilities-services/programs-and-policies
  Labeling of Chemical Substances
  Chemical Inventory
  Safety Data Sheets
  Hazard Identification
  Employee information and training

## Slide 8: Hazard Communication What you need to Know
SOME EXAMPLES OF HAZARDS ARE:
Corrosive (Acid/Base) – Irritates or burns skin or eyes
Toxic – May cause illness or death
Flammable - Readily catches on fire
Reactive – May react dangerously when mixed with incompatible substances
Compressed gas –Extreme pressure may be released
Carcinogen – May cause cancer

## Slide 9: Hazard Communication What you need to Know
Routes of entry
  Ingestion, Inhalation, Absorption, and Injection
All containers must be labeled
Health Hazards – acute vs. chronic
Safety Data Sheets
New GHS system has 16 sections
https://www.oswego.edu/facilities-services/environmental-health-and-safety

## Slide 10: Any Questions Understanding SDS?

## Slide 11: Asbestos
Regulated by:
  OSHA – 29 CFR part 1910.1001
  EPA – 40 CFR part 763
  DOT – 49 CFR part 173
  DEC – 6 NYCRR part 364
  DOH – 10 NYCRR part 73
  DOL – 12 NYCRR part 56

## Slide 12: Which of these is Asbestos?

## Slide 13: Asbestos The Good, The Bad, The Ugly, The Good
Strong, durable mineral resistant to fire and chemicals
Like many facilities built in the late 60’s early 70’s, present in some older buildings on campus
Long term exposure can cause asbestosis, lung cancer, mesothelioma
  Latency period is 15-40 years
We have a management plan

## Slide 14: Asbestos
Regulated in materials > 1% asbestos
  Can only be confirmed in a certified laboratory
Asbestos fiber 100 times smaller than the diameter of a human hair
Can be suspended in the air for up to 3 days
If the material is in good condition e.g. sealed, painted, it is not a risk to your health.
Two forms:
  Friable – easily pulverize in you hand (insulation)
  Non-Friable – unable to pulverize in your hand (floor tile)

## Slide 15: KNOW YOUR SUSPECT MATERIALS
Floor Tiles
Joint Compounds
Ceiling Tiles
Caulk
Spray-on Insulation
Wall and Ceiling Plaster
Mastic (glue)
Roofing materials
Wall and Ceiling Textures
Pipe Insulation

## Slide 16: Joint Compound

## Slide 17: Spray-on Fireproofing

## Slide 18: Signage

## Slide 19: Custodial Cleaning Activities Floors
Allowed
  Wet scraping wax removal
  Wet stripping/buffing
  Waxing
NOT Allowed
  Dry buffing
  Sanding, cutting, grinding
  Removal of loose tiles (STOP: Contact Supervisor)

## Slide 20: Custodial Cleaning Activities Textured Ceilings
Allowed
  Light wet wash
  Item removal if paint does not lift
  Routine lamp maintenance
  Smoke alarms (Maint. team only)
NOT Allowed
  Scraping loose material (STOP: Contact Supervisor)
  * If you see material that may have come from the ceiling, let your supervisor know.

## Slide 21: Custodial Cleaning Activities Walls
Allowed
  Washing painted surfaces
  Light wet scraping
  Adhesive hook removal (STOP if paint lifts, Contact Supervisor)
NOT Allowed
  Digging into substrate, gouging, sanding

## Slide 22: Asbestos Exposure – by the Numbers
OSHA Permissible Exposure Limit – 0.1 f/cc
Breathing Rate – 10 L air/min (8 L at rest 60 L during a run)
X 60 min = 600 L/hour
X 8hr shift = 4800 L/day
Convert to cubic centimeters X 1000 = 4,800,000 cc/day
X OSHA PEL of 0.1f/cc = 480,000 f/day

## Slide 23: Any Questions on Asbestos?

## Slide 24: Personal Protection Equipment
OSHA – 29 CFR 1910, 1915, 1926
Eyes/ face
Head
Foot
Hand
Hearing
Respiratory

## Slide 25: Basic PPE
Office
  Business casual
Grounds
  Sturdy leather work boots/shoes & long pants
Custodial
  Closed-toed shoes. No tank tops.
Head phones – At the discretion of the supervisor.

## Slide 26: Noise in Your Work Environment
OSHA Designated Exposure Limits
  85 dBA - Action Level for HCP
  90 dBA - Permissible 8-hr. TWA
Two-Foot Rule (Arms Length)
Wear Hearing Protection when doing loud tasks – ask your supervisor where to get some earplugs

## Slide 27: Grounds – Hazard Analysis for Trimmer (Weed-Eater)
Eyes (glasses)
Ears (plugs)
Feet (work shoes)
Legs (long pants)
Head (hard hat)
Vibration (gloves/ alternate hands)
Heat exhaustion (fluids)
Sun (sun screen)
Traffic (vest)
Bees/Ticks (repellent)
Poison Ivy (clothing)
Pollen (dust mask)
Lightening

## Slide 28: Custodial – Hazard Analysis for Cleaning
Eyes (splash goggles)
Hands (gloves)
  Nitrile for chemicals
  Canvas or leather for general purpose
Heat Exhaustion (fluids)
Not PPE, but ensure lifting with legs, not back

## Slide 29: Fire Safety
Annual testing of Fire Alarms, Detectors, Sprinklers
  Do you still need to evacuate if there is a Drill?
  YES!

## Slide 30: Fire – Basic Systems

## Slide 31: Fire Emergency Response
Rescue – rescue other in immediate danger
Alert – Shout Fire! Or Pull fire alarm and Dial Emergency Phone number
    312-5555 from a cell or 911 from a campus phone
Contain – Close all doors
Evacuate – not Extinguish. Get out!

## Slide 32: Fire – Blocked Exit

## Slide 33: Heat Stress
Exposure to heat can cause illness an death.
Risks
  High temps, low breeze, direct sun
  Heavy physical labor
  Low water intake
  Recent alcohol or caffeine consumption

## Slide 34: Heat Exhaustion Symptoms
Headaches, dizziness, fainting
Weakness, cramps
Thirst, nausea, or vomiting

## Slide 35: Heat Stroke Symptoms
Confused, unable to think clearly, pass out, collapse, or seizures
May Stop Sweating – Emergency!

## Slide 36: Heat Stress Protection
Know symptoms; monitor yourself and others
Drink plenty of fluids before you are thirsty. Heat Index >100o F, have a pint of water per hour.
Minimize direct sun
Avoid beverages containing alcohol or caffeine
Wear lightweight, light colored, loose-fitting clothing

## Slide 37: Confined Space
OSHA 29CFR 1910.146
Area not designed for continuous occupancy
Limited egress
Dangerous atmosphere
Extraction plan and Attendant
Examples:
  Crawl spaces
  Manholes
  Ductwork

## Slide 38: Confined Space
Summer Students: Do not Enter !!

## Slide 39: Excavating/Trenching
OSHA 29CFR 1926.651
Excavations >4’ require:
  Competent Person
  Trench box or sloping
  Means of Egress

## Slide 40: Excavation/Trenching
Summer Students: Do not Enter or go near trench!

## Slide 41: Lockout/ Tagout
OSHA 29CFR 1910.147
Control of Hazardous Energy
  Electrical, mechanical, thermal, hydraulic, gravity
Isolates the energy during service

## Slide 42: Lockout/ Tagout
NEVER Remove!
Find a tag on floor, report it!

## Slide 43: Fall Protection
OSHA 29CFR 1926
Scaffolds
Extension Ladders
Step Ladders
Slips, Trips, Falls

## Slide 44: Scaffolds
Summer Students not allowed on scaffolding without additional training.
Coordinate with supervisor if necessary.

## Slide 45: Ladder Basics
Ladders must be inspected before each use.
Face the ladder when ascending or descending.
While climbing, maintain three points of contact at all times.
Keep your body centered on the ladder.
Never let your belt buckle pass either side rail.
Avoid setting ladders up in high traffic areas or barricade the area around ladder.
Do NOT use metal or aluminum ladders near exposed energized electrical equipment.

## Slide 46: Extension Ladders
  Inspect for good condition
  Ensure placement has good footing
  4:1 Ratio
  Falls — 349 out of 874 total deaths in construction in CY 2015 (39.9%)

## Slide 47: Step Ladders
Only use in the fully open position on firm level ground.
Do not use a stepladder that is folded or in a leaning position.
Never sit/stand on the top two rungs.
Consider work height when selecting a stepladder
  Falls — 349 out of 874 total deaths in construction in CY 2015 (39.9%)

## Slide 48: Step Ladders

## Slide 49: Slips, Trips, Falls
Eliminate Hazards – If you see something, correct it or talk to your supervisor
Common Sense
Warn others
Don’t climb on shelving or chairs

## Slide 50: Slips
Weather conditions and cleaning may cause floors to be wet.
Clean up spills immediately
Use signage and caution tape

## Slide 51: Trips
Eliminate clutter, cords
Be aware of uneven surfaces

## Slide 52: Bloodbourne Pathogens
OSHA 29CFR 1910.1030
Pathogens are infectious microorganisms in human blood that can cause disease – Hepatitis B, Hepatitis C, and HIV
Regulation developed mainly for healthcare personnel and first responders

## Slide 53: Bloodbourne Pathogens
Training provided to full time Custodial and Plumbing staff, NOT Summer Students
Program requires a series of shots and medical documentation
Summer Student Custodial staff will still be able to clean bathrooms but are prohibited from cleaning up visible blood. Contact supervisor if you encounter visible blood.
Do not treat someone who is bleeding

## Slide 54: Vehicles – Seat Belts

## Slide 56: Facility Services Safety It begins with YOU!

## Slide 57: Questions
EHS – 110 Lee Hall x 3157